Quarries National Joint Advisory Committee (QNJAC)

Plant Safety

Information Sheet 4

March 2012

Fork Lift Trucks (FLT)

Maintenance and Safety Checks

This Information Sheet has been developed by the Quarries National Joint Advisory Committee (QNJAC) to help quarry operators, contractors, managers and others learn how to make health and safety improvements in the quarry industry. This guidance represents good practice, which may go further than the minimum you need to do to comply with the law.

Approved by the Quarries National Joint Advisory Committee (QNJAC) – Version 1: Date 28 March 2012

USE OF THIS BOOK

The purpose of this book is to ensure that all vehicles operated at sites are maintained in safe condition. Its use is purely voluntary and it should be tailored to your site specific needs. Maintenance and safety checks are to be made as soon as practicable when a machine is used. Local rules will provide more detail.

The book shall be retained in the vehicle cab and be available at all times for inspection. If the book is lost or damaged, report it immediately to your supervisor/manager.

- Enter the vehicle make and type and plant number on the front cover and at the top of each sheet used.

- All items must be meaningfully addressed with the appropriate box receiving a () if in order, a cross () if requiring attention or a zero (0) if not applicable. The defects box requires a yes or no entering.

- The operator shall initial the sheet for each day.

- At the end of each week, the sheet shall be signed by the operator and the supervisor/manager. The top white sheet is then removed and filed in line with local rules.

- When the book is full, it shall be handed back to the supervisor/ manager and a new one requested.

# DEFECT REPORTING

- All defects shall be recorded in the defects section at the back of the book and be reported to the supervisor/manager in line with local rules.

- Where a defect is likely to affect the safe operation of the vehicle, e.g. brakes, steering, reversing aids, horn, lighting during darkness, the defect sheet must be completed and the book handed back to the supervisor/manager before the machine is put to work (or continues to work if a defect occurs during a shift).

- Where the supervisor/manager deems the machine is safe to continue working, he shall make a note of his reason on both copies of the defect sheet before acknowledging receipt and removing the top copy from the book.

- Where a defect sheet is received by the supervisor/manager, it shall be given a job reference number (top right hand box).

PRE-START CHECKS

| Area to be inspected | Recommended checks |
| --- | --- |
| Tyre Pressure | Check as per manufacturers recommendations WEEKLY |
| Tyre Condition (visual) | No obvious punctures, lack of air pressure, dangerous damage to tread or sidewalls. |
| Oil, Fuel and Coolant Levels | Check as per manufacturer’s recommendations |
| Oil, Fuel and Coolant leaks | Visual check for any significant leaks |
| Brakes | Check operation in forward and reverse, check park brake function |
| Fluid Levels | Check brake fluid levels and signs of leaks |
| Operating lights | Check operating lights are functional and clearly visible |
| Brake Lights | Check operation of all brake lights |
| Flashing beacon | Check if flashing beacon is fully operational |
| Cracks and damage to forks | Visually examine forks and attachments for obvious cracks and distortion |
| Carriage plate | Inspect for obvious cracks and damage |
| Forks/arms | Inspect for obvious cracks, obvious defects |
| Adjustment pins | Pins in position and secure |
| Load guard | In place and good condition |
| Mast/ roller/ sliders | Check channels and runners for obvious wear, scratches/ scoring |
| Lift chains and pulleys | Obvious loose or worn pins or links |
| Capacity plate | In position and legible |
| Operating seat/position/ seatbelt | Check seat is in good operational condition, including adjustment. Inspect seat belt and securing points |
| Steering gear | Check operation, check for no excessive freedom or stiffness |
| Directional controls | Present, legible and fully operation |
| Mirrors | Inspect mirrors and in position and visibility is clear through all fitted |
| Footbrake and parking brake | Verify operation of footbrake and parking brake, report on decrease in performance |
| Overhead guard | Inspect overhead guard is in position and in good operational condition |
| Windows and wipers | Inspect windscreen for cracks and cleanliness, check wipers are fully operation including washer operation |
| Reverse warning system (if applicable) | Fully operational and audible |
| Horn | Fully operational and audible |
| Lift/ lower, tilt and side shift | Operate and check if working correctly |
| Electric trucks – mains/ charger off | Charging point in good condition and switched off |
| Electric trucks - Disconnect leads | Inspect leads for general condition |
| Electric trucks - Electrolyte levels | Visual examination of levels |
| Gas trucks – condition of gas valve and supply line | Pipe is not cracked and installed correctly onto gas bottle, no obvious smell of gas |
| Gas trucks – propane tank securing strap | Securing strap in good condition, bottle secured onto truck |
| Propane tank/ damage corrosion | Check for obvious visual condition |

| FORK LIFT DAILY SAFETY CHECK SHEET |
| --- |
| Driver's Name…………………………………………………….… | Plant No………………………..……………….………... |
| Make…………………………………………………………..……….. | Type………………………………………………….…… |
| Week Commencing…………………………………………………. | Hours……………………………………………………... |
| Inspection if applicable | Mo | Tu | We | Th | Fr | Sa | Su |
| Tyre Condition & Wheel nuts (visual) |  |  |  |  |  |  |  |
| Tyre Pressure (once weekly) |  |  |  |  |  |  |  |
| Engine & Hydraulic Oil |  |  |  |  |  |  |  |
| Radiator Coolant |  |  |  |  |  |  |  |
| Fuel |  |  |  |  |  |  |  |
| Brake fluid |  |  |  |  |  |  |  |
| Operating Lights |  |  |  |  |  |  |  |
| Brake Lights |  |  |  |  |  |  |  |
| Flashing Beacon |  |  |  |  |  |  |  |
| Cracks & Damage |  |  |  |  |  |  |  |
| Carriage Plate |  |  |  |  |  |  |  |
| Forks Arms |  |  |  |  |  |  |  |
| Adjustment Pins |  |  |  |  |  |  |  |
| Load Guard |  |  |  |  |  |  |  |
| Mast, Roller, Sliders |  |  |  |  |  |  |  |
| Lift Chains and Pulleys |  |  |  |  |  |  |  |
| Capacity Plate |  |  |  |  |  |  |  |
| Operating seat / Position & Seatbelt |  |  |  |  |  |  |  |
| Steering Gear |  |  |  |  |  |  |  |
| Directional control |  |  |  |  |  |  |  |
| Mirrors |  |  |  |  |  |  |  |
| Footbrake & Parking Brake |  |  |  |  |  |  |  |
| Overhead gurad |  |  |  |  |  |  |  |
| Windows / Wipers |  |  |  |  |  |  |  |
| Reverse warning system (if applicable) |  |  |  |  |  |  |  |
| Horn |  |  |  |  |  |  |  |
| Lift & Lower, Tilt and side shift |  |  |  |  |  |  |  |
| Mains & Charger off |  |  |  |  |  |  |  |
| Disconnect Leads |  |  |  |  |  |  |  |
| Electrolyte Levels |  |  |  |  |  |  |  |
| Condition of Gas Valve and supply line |  |  |  |  |  |  |  |
| Propane tank securing strap |  |  |  |  |  |  |  |
| Propane tank damage / corrosion |  |  |  |  |  |  |  |
| Job/ Defect number |  |  |  |  |  |  |  |
| Comments: |
| Operator: | Supervisor/Team leader: |

##### DEFECT ACTIONS

CATEGORY A

When defects with any of the following occur the vehicle MUST be taken out of service immediately and reported.

- Reverse warning systems (where fitted)

- Brakes

- Steering

- Front windscreen cracks in line of vision

- Mirrors

- Headlights in hours of darkness or poor visibility

- Vehicle/ attachment structure

- Potentially dangerous tyre damage

- Any warning device

- Wipers and washer operation

- Major oil or fuel leaks

- Damaged seat where the integrity of the seat is compromised

- Guards damaged or missing

- Door handles (operating devices) which prevent efficient opening

- Seat belts, damage of any kind

- Park brake

- Brake lights

- Flashing beacons

# CATEGORY B

When defects with any of the following occur the management MUST be informed immediately and arrangements made to rectify the defect overnight or A.S.A.P

- Indicators

- Headlights in hours of daylight

- Any minor cracking to windscreen

# CATEGORY C – 1 Month

Anything else that is not mentioned above and is not considered a safety hazar

| Vehicle Defect Report: | Job Ref No: |
| --- | --- |
| Machine: | Plant No: |
| Defect: |
| Reported by: | Date: |
| Received by: | Date: |
| Remedial Action Taken: |
| Fitter’s Signature: | Date: |
| Manager/Supervisor: | Date: |

FORK LIFT DAILY SAFETY CHECK

MACHINE:

PLANT NO:

THIS BOOK SHOULD BE HANDED TO AND SIGNED BY THE MANAGER ON A WEEKLY BASIS

This document has been developed by the Quarries National Joint Advisory Committee (QNJAC) to assist in making health and safety improvements in the quarrying industry. This guidance may go further than the minimum you need to do to comply with the law. It is not intended to be fully comprehensive and you may need to tailor it to your specific requirements.