Speakers Notes – silica dust

This talk focuses on improving quarry operatives and maintenance personnel understanding of the risks of exposure to silica dust in the workplace.

The presentation can be run from a laptop or printed and used.

Note – A number of short video clips can used as part of the presentation. These will need to be downloaded separately.

Background

Silica dust is a natural mineral present in large amounts in things like sand, sandstone and granite. Silica material when crushed or abraded during quarrying activities  creates a very fine dust known as respirable crystalline silica (RCS) dust but is also often called silica dust.

Anyone who breathes in workplace silica dust should know the damage that can be done to their lungs and airways, and should therefore have an understanding of the importance of control measures and the need use them properly.

Format

The talk is divided into four topic sections with each section lasting approximately 10 minutes:

- Understanding silica dust

- Where exposure to silica dust can occur in the workplace

- Health effects - how exposure to silica dust could effect the body

- What can be done to prevent or control exposure to silica dust

The final section summaries the “myths and realities” of dust; “your responsibilities” and the key messages, the information in this slide can be issued at the end of the talk for workers to go away with (see Appendix 1).

Appendix 2 provides a template for recording attendance.

Before you start

Please take a little time to prepare, read through the tool box talk and speakers notes. Check its content against your own knowledge of the topic and be committed to what you are going say. It is important that who ever delivers the talk is comfortable with the language used in the presentation. Keep it simple and be consistent with your key messages.

Identify the workers who should listen to the talk and who will be able to put what they hear into practice.  Arrange to hold talks in a good location away from noise and distraction.

Using the talk

The talks allow you and the workers to explore the risks of exposure to silica dust in the workplace and think about ways to deal with it. Remember – focus on the main key points you want the listeners to keep in mind when they return to their workplace!

SLIDE 1 SLIDE 1 What to say This talk focuses on improving workers understanding of the risks of exposure to silica dust in the quarry workplace. Training is aimed at quarry operatives, including contractors and maintenance personnel. The aim is to provide you with an overview of silica dust, gain an understanding of the health effects of possible exposure to workplace silica dust and the control measures to reduce exposure to silica dust. Introduction: Silica is a natural mineral present in large amounts in things like sand, sandstone and granite. Silica material when crushed or abraded during quarrying activities creates a very fine dust known as respirable crystalline silica (RCS) dust but is also often called silica dust. Anyone who breathes in this workplace silica dust should know the damage that can be done to their lungs and airways, should understand the importance of control measures and the need use them properly. Please note: This talk does not cover the regulations: The Control of Substances Hazardous to Health Regulations 2002 (COSHH) or the Workplace Exposure Limit (WEL) for Respirable Crystalline Silica (RCS)

SLIDE 2 SLIDE 2 What to say Domestics will be dependent on the location of the talk and the audience. Cover: nearest toilets, evacuation procedure - is a fire alarm test planned? This talk will last approximately 1 hour with time for a Q&A session.

SLIDE 3 SLIDE 3 What to say The talk is divided into four sections. The key learning points for today’s session are understanding: Understanding silica dust Where YOU might be exposed to workplace silica dust Health effects - how exposure to silica dust could effect YOUR body What YOU can be do to prevent or control exposure to silica dust Has anyone attended a talk on dust before? Does anyone here understand the risks associated with exposure to workplace dusts? Is workplace dust just a nuisance or can it be hazardous to health? This talk focuses on YOU as the individual worker to gain an understanding of what YOU can do to protect yourself from exposure to silica dust.

SLIDES 4 to 6 SLIDES 4 - 6 Read through the text provided on each slide to explain the nature of silica dust SLIDES 7 – 8 SLIDE 7 Read through with the audience the Myth and Reality of exposure to silica dust What to say “Always doing it this way” has not helped stop workers developing lung disease continuing doing it “this way” means you could be exposed to silica dust. SLIDE 8 What to say This is an opportunity for us to discuss as a group what work activities we think can lead to exposure to silica dust? Do you know where possible workplace exposure can occur? Question? If correct control practices are not implemented what activities could be considered high risk? SLIDE 9 SLIDE 9 What to say This diagram illustrates the different processes or activities in a quarry environment where silica dust exposures can be high. (Read out the activities listed) SLIDE 10 SLIDE 10 What to say These video clips show a work activity that creates dust and how by using Tyndal lighting the dust that the worker is exposed to becomes more obvious. Although these video clips are not directly about quarry working, the point is they do show the dust that people do not always see. This will be the same for working in a quarry. Please note: The two video clips are not embedded into presentation and will need to be downloaded separately.

SLIDES 11 – 12 Slide 11 Read out the text in myth and reality What to say SLIDE 12 Respiratory disease statistics are based on past exposures and the evidence about the extent of silica related ill health takes different forms, each of which has its own strengths and limitations. These statistics give an indication of the scale of exposure to RCS in the workplace in comparison to fatal workplace injuries. SLIDES 13 - 14 SLIDE 13 What to say This short video clip shows the routes of entry for respirable dust. Please note: The video clip is not embedded into presentation and will need to be downloaded separately. What to say SLIDE 14 Exposure to silica dust can put you at risk of developing Silicosis. Silicosis is a serious disease and can take years of exposure to silica dust to develop but high exposure can significantly speed up this process. Slide 15 What to say (Read out symptoms listed) Slide 15 Unprotected exposure can lead to irreversible lung damage and respiratory disease. Symptoms can also include a cough and difficulty breathing. Remember – report any symptoms to management immediately. Slides 16 - 17 What to say (Read out myth and reality) SLIDE 16 Re-consider the way you work. Silica dust is not just a nuisance or part of your job. Stop and think - silica dust exposure can be a health hazard. What to say Slide 17 This short 3 minute video called “Don’t be a dummy” features an experiment to show that it’s not always possible to tell if the air is safe to breathe just by looking at it. (Play video) Please Note: The video clip is not embedded into presentation and will need to be downloaded separately Slides 18 – 20

SLIDES 21 Slides 18 – 21 This section covers controlling exposure to dust. Read out the information provided in each slide What to say ‘EESI!’ (acronym for saying its “easy”) Enclose Extract Suppress It! Key messages on controlling exposure are: Always confirm that the dust extraction is turned on and working Always confirm that water suppression is turned on and working Always confirm control cab air supply is turned on and working Keep doors and window closed when working Look for signs of leaks, wear and damage every day If you find a problem with equipment report it - don’t just carry on working Keep work area clean Leave powders to settle and compact inside the silo before bagging Clamp the bag securely to bagging head during filling Are you sure how to use all dust controls? If not tell your supervisor – don’t just carry on working. Slide 22 - 23 What to Say Slide 22 Housekeeping should include routine cleaning up. Indicators of a problems or warning signs include silica dust on surfaces of machines, window sills, on clothing and dust build-ups in the vicinity of conveyor or transfer points. Everyday clear up accumulated waste Use wet cleaning, damp down or use vacuum cleaning equipment fitted with high-efficiency filters for cleaning up fine dusts rather than shovelling or brushing. Dispose of waste dust safely What to say Slide 23 Never use compressed air for removing dust from clothing. Using compressed air to remove dust creates clouds of dust; the dust becomes airborne and moves closer to your breathing zone. Slide 24 – 25 What to say Slide 24 Although RPE should not be needed if the controls work properly. Sometimes RPE is likely to be your final option and is an extremely important part of the overall strategy to minimise your personal exposures. Check your RPE works properly every time you use it Use, maintain and store your protective equipment in accordance with instructions What to say Slide 25 Exposure to silica dust depends on many factors: The proportion of silica in the material; the mechanical work involved in breaking up and processing; individual work patterns; the measure taken to prevent or control dust. What is critical is that if you as workers continue to breathe in silica dust over your working life then eventually you can damage your lungs – once damaged is done it cannot be reversed. Slide 26 What to say Slide 26 Remember these myths and think about the reality……. Remember stone dust can be harmful, respiratory disease can take years to develop, control exposure now! Slide 27 Please note: The information provided in this section can be to issue at end of training session. See Appendix 1 What to say Key messages: Regularly breathing in silica dust can wreck your life. It could permanently damage your lungs, ruin your quality of life as you get older and cause you to die early. You need to make sure that you protect yourself from the harmful effects of breathing in silica dust. Use the available suppression and extraction systems to reduce the amount of dust created and limit its spread. Look for signs of leaks, wear and damage every day. If equipment is faulty or broken fix it or tell someone who can sort it. Look after your kit and it will look after you. Regularly clean equipment and masks and store your kit in a clean place away from dust. Change and clean your work wear regularly; don’t use airlines to blow dust from your clothing or equipment. Ask about further training so that you can find out more about the things you can do to reduce the risks of breathing in silica dust. For more information visit: www.safequarry.com http://www.hse.gov.uk/quarries/hardtarget/dust.htm http://www.nepsi.eu/agreement-good-practice-guide/good-practice-guide.aspx Slide 28 - 29 What to say This is the final session giving us an opportunity to discuss as a group what steps can be taken to reduce exposure within the working environment? What can we take away from today’s talk? What can we do differently in the workplace to help reduce exposure to silica dust? How can we protect ourselves?

Appendix 1

Key messages:

- Regularly breathing in silica dust can wreck your life. It could permanently damage your lungs, ruin your quality of life as you get older and cause you to die early.

- You need to make sure that you protect yourself from the harmful effects of breathing in silica dust.

- Use the available suppression and extraction systems to reduce the amount of dust created and limit its spread. Look for signs of leaks, wear and damage every day.

- If equipment is faulty or broken fix it or tell someone who can sort it.

- Look after your kit and it will look after you. Regularly clean equipment and masks and store your kit in a clean place away from dust.

- Change and clean your work wear regularly; don’t use airlines to blow dust from your clothing or equipment.

- Ask about further training so that you can find out more about the things you can do to reduce the risks of breathing in silica dust.

- For more information visit:

www.safequarry.com

http://www.hse.gov.uk/quarries/hardtarget/dust.htm

http://www.nepsi.eu/agreement-good-practice-guide/good-practice-guide.aspx

Appendix 2

It is good practice to keep a record of who has heard the talk and when. This template may be helpful

Record of attendance

| Company |  |
| --- | --- |
| Location |  |
| Trainer |  |

To confirm attendance of Tool Box talk on ‘silica dust’ covering: understanding silica dust; exposure to silica dust; health effects and controlling exposure to silica dust

| Date | Name | Job title |
| --- | --- | --- |